| أولا": الهدف: توريد أنابيب مبادلات حرارية نحاسية مزعنفة. ثانيا": المواصفات الفنية: الأنبوب الأساسي: المعدن : أنابيب نحاس خلائطي مسحوبة مطابقة للستاندر الأمريكي ASTM – B111- UNS NO : C44300 أو ما يعادله. الابعاد والكميات : القطر الخارجي (مم) الطول (مم) السماكة مم الكمية (انبوب) 25 6010 2.5 400 الزعانف: - الأبعاد: القطر الخارجي (مم) النوع السماكة ( مم) عدد الزعانف بالانش 52 G(Wound Up) 0.3-0.4 10 المعدن:- ألمنيوم . نهايات حرة للأنابيب بدون زعانف لمسافة (50 -55 ) مم ثالثا": متطلبات عامة: تقارير الاختبار للمواد المطلوبة مطابق للستاندر الأمريكي ASTM – B111- UNS NO : C44300 - يجب أن تقدم تقارير نتائج الاختبارات مع المواد الموردة. . يجب أن يكون تغليف الأنابيب بحري ضمن صناديق خشبية حسب الستاندر الأمريكي : ASTM A700- 05 fig10 مدة الضمان : عام ميلادي بدءا" من الاستلام الأولي . يجب على العارض أو المصنع أن يكون معتمدا" من قبل منظمة الجودة العالمية أو مقاييس إدارة الجودة سلسلة نظام (ISO 9000) . وهذه الشهادة يجب أن تكون صالحة وقابلة للتطبيق على المواد أو الأجهزة المطلوبة . وعلى العارض أن يضمن عرضه نسخة من هذه الشهادة. مدة التوريد : 6 أشهر واصل أرض المصفاة | I- Objective: Supplying Of Heat Exchanger Copper Finned Tubes. II- Technical Specifications: 1. Core Tube: -Material: Copper alloy seamless tubes according : ASTM – B111- UNS NO : C44300 or Equivalent. - Quantities And Dimensions: 2. Fins: - Dimensions Quantity (tube ) Total Length (mm) Thickness (mm) OD (mm) 400 6010 2.5 25 OD (mm) Type Thickness (mm) Fins/Inch 52 G(Wound Up) 0.3 - 0.4 10 Material :Aluminum . Free ends( Without Fins) : (50-55)mm III. General Requirements: 1.Test reports for required materials according to : ASTM – B111- UNS NO : C44300 - Results of test reports should be submitted with the delivered materials. 2 Seaworthy Packing in wooden cases according to ASTM A700 -05 fig 10 3. Guarantee: One year from the date of primary Receipt. 4.The bidder or manufacturer must be approved by an internationally recognized management system standard (ISO 9000) series .This certificate must be valid and applicable to the offered materials. A copy of this certificate should be submitted in his offer. 5. Delivery Period : 6 months (warehouses of Homs Refinery ) |
| --- | --- |

م.أحمد العلي     م. رامي كرامي   م . وديع السبعة        م . منذر السبعة          م. هيثم مسوكر               يعتمد  المدير العام بالتكاليف

م . هيثم بهجت مسوكر