| المواصفات الفنية للبطاريات القلوية لمحطة القوى الجديدة (31B) | Technical specification of alkaline Batteries (31B). |
| --- | --- |
| 1-بطاريات قلوية نيكل_كادميوم مزودة بفتحة علوية والبطاريات يجب أن تكون مفرغة،فارغة وجاهزة. 2- بطاريات نيكل_ كادميوم غلاف بلاستيكي مقاوم للصدمات والكسر وتغير درجات الحرارة سعة(250)أمبير ساعي العدد الكلي(800)بطارية. 3-المواد اللازمة للبطاريات: هدر وكسيد البوتاسيوم النقي وهدر وكسيد اللييثيوم اللازمة للبطاريات كمواد صلبة من أجل تعبئتها أول مرة. 4-تقديم الوثائق الكاملة من منحنيات تفريغ وتعليمات تشغيل باللغة الانكليزية أو العربية وشهادة اختبار. 5-مدة الضمان(12)شهرا ميلاديا من وضع البطاريات بالخدمة أو(18)شهرا ميلاديا من تاريخ الاستلام0 6-على العارض أن يرسل نموذج من البطاريات المذكورة أعلاه للنموذج المعروض خلال الدراسة الفنية وقبل التفريغ الفني مع المواد اللازمة (هدر وكسيد البوتاسيوم وهدر وكسيد اللييثيوم). 7-على العارض تقديم الوصلات المعدنية بين الخلايا مع احتياطي 20%. 8- على العارض تقديم عدة عمل وصيانة للبطاريات(مقياس كثافة عدد أربعة وأفومتر نوعية جيدة عدد أربعة). 9-يجب أن تكون البطاريات عند تسليمها حديثة الصنع ولم يمض على تاريخ صناعتها أكثر من ستة أشهر. عدنان الحموي م. حيان ريشة رئيس اللجنة م . عبد الرحمن الهميش | 1-Nickel_cadmium_alkaline batteries with top vents ,the cells must bed's charged ,emptied and ready . 2--Nickel-cadmium batteries plastic cells must be Resistance to mechanical abuse and ant broken and wide operating temperature range capacity (250)A/h total number (800) cell. 3-The required materials for batteries: Pure potassium Hydroxide with the necessary additives of lithium Hydroxide in solid from sufficient for the first filling of all required cells. 4-Instruction and discharge curves, document's in English or Arabic and test certificate should be submitted. 5-Guarantee period should be (12)A.D month At least as of batteries fitted, or (18) A.D month as of delivery report date. 6-The bidder should offer a sample of the batteries mentioned above with the required materials of this sample during the technical study and befor the technical evaluation (potassium Hydroxide and lithium Hydroxide). 7-The bidder should submit metallic connection between the cells with reserve 20%. 8- The bidder should submit action and maintenance tools with the cells(density Quantity fore measure Quantity fore voltmeter good quality Quantity. 9-The batteries should be newly manufactured. Manufacturing date must not Exceed six months at the date of delivery to the refinery. END |